LoRa Temperature Sensor

# Requirements
- Power source is a 18650 lithium battery (future iteration will use solar panel)
- Device can recharge battery
- Device has protections against battery overdischarge and short circuit.
- Temperature measurement does not have to be precise
# Architecture

# Component selection
LDO
Name	Vmin	Vmax	Amax	Iq	Vdrop	Price
STLQ020	2V	5,5V		300nA	160 mV	0,51 eur
MCP1810T-25I/TT	2.7V	5.5V	150mA	20nA	380mV	0.42 eur

Battery protection ICs
Name	OverDischarge V	Overcharge V	Iq	Overcurrent protection	prices
DW01A	2.5V	4.3V	3uA	Yes	$0.05
HY2113	2.00 to 3.10V	4.0 to 4.5V	3uA	Yes	$0.09
FS312F	2.9V	4.25V	3uA	Yes	$0.11

Battery charger ICs
Name	Target V	I charge	Iq	Price
TC4054T	4.2V fixed	Up to 500mA	2uA	$0.05

Mosfet for battery protection 2 N-Mosfet needed with maximum internal resistance of 150mOhm
Name	Vmax	Imax	Iq	V drop	price

# TODO
- Check uC voltage against RFM95
  STM: 1.65 V to 3.6 V
  RFM95: 1.8 to 3.7 V - 120mA
- Decide for switching voltage supply or just an LDO
  Since the device is going to stay mostly inactive, it is better to use a regulator with very low quiescent current. LDO MCP1810 is the best solution.
- Research about battery charging/protection circuits